BCD numbers (binary coded decimal) are represented by a mantissa,
sign and exponent fields.  There are two kinds of BCD numbers in 
the HP 48SX, 12-form and 15-form BCD numbers, called BCD12 and
BCD15 in the field descriptions.

Both kinds have several things in common:

    *    A mantissa.  Each digit of the number is represented by 
         one nibble in the mantissa.  12-form BCD numbers have a
         12 digit mantissa and 15-form BCD numbers have a 15
         digit mantissa.  There is an implied decimal point after
         the Most Significant Digit (msd) with respect to the 
         exponent.

    *    A sign nibble.  Positive numbers are represented by a 
         0 and negative numbers are represented by a 9.

    *    An exponent.  The exponent is in 10's compement.
         12-form BCD numbers have a 3 nibble exponent and 15-form
         BCD numbers have a 5 digit exponent.

12-form BCD numbers are the basis for Real Number, Complex 
Number, Real Array and Complex Array data types.

15-form BCD numbers are the basis for Long Real and Long
Complex data types.

BCD12:

 15 14                     3  2   0
+--+------------------------+------+
|S | msd..  Mantissa  ..lsd | Exp  |
+--+------------------------+------+
 1             12              5

BIN15:

 21 20                           5  4       0
+--+------------------------------+----------+
|S | msd...    Mantissa    ...lsd |   Exp    |
+--+------------------------------+----------+
 1                15                   5

------------
This is from my 'HP 48SX Internals' document that is getting close to its
first posting.  Hope it helps.

Take a look at the Real Number and Long Real objects starting with 
0 (Real Number) at 2A2B4 to 10 (Long Real) at 2A596.  There are 34
objects in that range.  Most are simple.  But includes PI and MAXR...

    Derek S. Nickel