NOTE : In order to store the files in the NPDSA archive, their names have been
changed to correspond to the standard format. You will need to change the names
to the following to match the description in this document.

a02tcc.boo	->	tcc.boo
a02getshar.exc	->	getshar
a02mkboot.exc	->	mkboot
a02sh.hex	->	sh_x
a02dehex.hex	->	dehex_x
a02shar.hex	->	shar_x
a02unpack.exc	->	unpack
a02tcc1.sha	->	tcc1.sha
a02tcc2.sha	->	tcc2.sha
a02tcc3.sha	->	tcc3.sha
a02tcc4.sha	->	tcc4.sha


 

                   Small-C compiler for the BBC Micro

                              Release 0.70

                         A.J.Travis  01-May-89


INTRODUCTION

Small-C is a subset of the C programming language for which a number of
public-domain compilers have been written.  The original compiler was
written by Ron Cain and appeared in the May 1980 issue of Dr.Dobb's
Journal.  More recently, James E.Hendrix has improved and extended the
original Small-C compiler and published "The Small-C Handbook", ISBN
0-8359-7012-4 (1984).  Both compilers produce 8080 assembly language,
which is the most popular implementation of Small-C to-date.  My 6502
Small-C compiler for the BBC Micro is based on "RatC", a version of the
original Ron Cain compiler described by R.E.Berry and B.A.Meekings in "A
Book on C", ISBN 0-333-36821-5 (1984).  The 6502 compiler is written in
Small-C and was bootstrapped using Zorland C on an Amstrad PC1512 under
MSDOS 3.2, then transferred onto a BBC Micro using Kermit.  The compiler
can be used to cross-compile 6502 code from an MSDOS host, or as a
'resident' Small-C compiler on a BBC Micro. 


DEVELOPMENT

I started to implement a Small-C compiler for the BBC Micro in 1985
because I wanted an alternative to assembly language or Forth for
writing 6502 image processing software.  I was very impressed by the
performance and portability of Forth, but found the language difficult
to use.  I was aware that a sub-set of Pascal had been implemented in
Forth, and I set about developing my own version.  However, I quickly
realised that the virtues of using a threaded-code interpreted language
(TIL) could be exploited just as easily by generating code for an
interpreter conventionally, instead of using Forth itself to generate a
'target' vocabulary.  I began to use 'C' and Unix on a DEC pdp11 at the
time and I decided to implement a sub-set of C, instead of Pascal, on
the BBC Micro after reading "The Small-C Handbook" by Hendrix and "A
Book on C" by Berry and Meekings.

I began by implementing "Rat-C" under Unix on the pdp11.  The Rat-C
compiler is much smaller than the Hendrix compiler, and it also produces
'generic' assembly code.  I wrote a translator for the generic code
output by RatC, which generated 'JSR-threaded' code for the 6502.  A
JSR-threaded code interpreter is a form of TIL that uses the hardware
call-return mechanism of the processor as the low-level interpreter and
is the most efficient way of implimenting a TIL.  The code generated was
too verbose to produce a resident Small-C on the BBC Micro with only 29K
of usable memory in mode 7, but I was able to develop the run-time
support for the threaded-code interpreter and code generation model for
the 6502. 

Because of the severe memory constraints of a 'standard' BBC Micro, I
decided to translate Rat-C into BBC Basic in order to produce a resident
Small-C compiler that would run in 29K.  This 'tiny' C compiler ("tcc")
in BBC Basic was intended to be a 'bootstrap' for a Small-C version of
the 6502 compiler, and I began distributing copies of the Small-C to
friends and colleagues.  Eventually, I sent a copy of the compiler to
Chris Adie at Edinburgh University Micro Support Unit, and later to Alan
Philips at the Lancaster University Micros Software Distribution
Service. 

After several more releases of the "tcc" compiler, I was approached by
John Evans of Mijas software for permission to sell the Small-C as part
of his 6502 assembly language development system.  I was pleased to give
Mijas permission to use my code, which they have adapted for use with
the Mijas 6502 symbolic debugger.  I continued to develop the 6502
Small-C by optimising the code-generator for the 'small-machine'
environment of the BBC Micro and, during this development, I replaced my
earlier BBC Basic programs with Small-C versions.  Finally, I have
produced a resident Small-C for the BBC Micro that can also be used as a
cross compiler for the 6502 on an MSDOS host. 


RELEASES

	0.10  Jan-86  Original version
	0.20  Apr-86  Limited distribution
	0.30  Jul-86  Sent to Chris Adie at ERCC
	0.40  Oct-86  First version sent to <micros@lancs.vax1>
	0.41  Oct-86  Bug-fix release
	0.50  Dec-86  First version used by Mijas
	0.51  Apr-87  Limited distribution
	0.60  Jul-88  First DOS cross-compiler
	0.61  Dec-88  BBC Micro/Master language ROM
	0.70  Apr-89  Current release


CHANGES FROM RELEASE 0.5

Release 0.6 of the 6502 Small-C compiler was cross-compiled on an MSDOS
host and has been modified to avoid major incompatibilities with full
'C'.  Previous BASIC programs, including the compiler itself, have been
re-written in Small-C.  The Zorland C compiler objects to many of the
'liberties' I have taken with full 'C' usage, but compiles the Small-C
programs correctly.  An MSDOS distribution is also available containing
executable binaries of the Small-C compiler and 6502 assembler. 

Release 0.61 was a bug-fix release with corrected sideways ROM startup
code and corrections to the "shar" program for extracting shell
archives.  The formatted input functions atoi(), scanf(), fscanf() and
sscanf() have been added to the compiler library in this release, and I
have fixed a bug in "as65" which failed to detect certain illegal
expressions in opcode operands.

The Small-C release 0.70 language ROM works correctly on a BBC Master,
and several minor bugs have been fixed in the run-time library.  This is
the first version in which the Small-C command shell is used to compile
and run C programs.  I have also adopted lower-case mnemonics for the
6502 assembler, and extended the range of pre-processor directives
supported by "tcpp".


ACKNOWLEDGEMENTS

I am grateful to Jon Welch, and Dave Prosser from the Department of
Electronic Engineering at Bradford University who weeded out many of the
bugs in release 0.41 of the compiler.  I am also grateful to Alan
Philips at Lancaster University, and Rob McRon at Edinburgh University
for their help in distributing the compiler over electronic mail
networks.  A version of this compiler is distributed, with my
permission, by Mijas Software as part of a 6502 assembly language
development system for the BBC Micro.  I would like to thank John Evans
of Mijas for his interest in the compiler which he has extended and
adapted for use with the Mijas 6502 symbolic debugger.


COPYRIGHT

The programs in this distribution remain copyright (c) 1989 A.J.Travis,
and should not be used for any commercial purpose without prior consent
in writing.  The programs may be copied and further distributed for
non-commercial use without restriction, provided a copy of this notice
is also included. 


AVAILABILITY

Send an SAE and Acorn DFS formatted, double-sided 80 track 5.25" floppy
(or 360K DOS formatted, 5.25" floppy for the MSDOS version). 
Alternatively, mail me as <ajt@uk.ac.sari.rri> for an e-mail version. 

	Home address:				Work address:

	1 St. Nathalan Crescent,		Rowett Research Institute,
	Banchory,				Greenburn Road,
	Kincardineshire.			Bucksburn,
	AB3 3YU					Aberdeen.
						AB2 9SB

	tel. Banchory 2392			tel. Aberdeen 712751 x134
	

REQUIREMENTS

The "tcc" Small-C compiler requires a 'standard' BBC Micro or BBC Master
and a twin double sided 80-track disk drive in order to recompile
itself.  The run-time support routines and compiler library are
contained in a Small-C language ROM/RAM image that must be present in
order to use the compiler, but stand-alone versions of programs are
readily produced using a compiler option.  Source programs are edited
using Acornsoft VIEW or a similar editor, and any machine code
monitor/debugger can be used on the object programs produced. 


DOWNLOADING SHELL ARCHIVES

Several people have reported difficulty in downloading the BBC Micro
Small-C as Unix 'shell' archives.  These are simply a convenient way of
distributing programs over e-mail networks and BBS's.  The "unpack"
utility is intended to simplify the task of unpacking the archives after
downloading them onto BBC Micro disks.  Two blank formatted 80-track
disks are required to download and unpack the archives.  First, download
the kermit takefile "getshar" onto drive 0: and use it to download the
shell archives:

>					; BASIC prompt
> *xoff					; disable ARIES B32 shadow RAM
> <break>				; press break key
> *rload kermit 13			; load kermit ROM image in slot 13
> <break>				; initialise ROM
> *kermit				; invoke kermit
BBC>					; kermit prompt
BBC> set file type ascii cr		; setup for ascii transfer
BBC> get getshar getshar		; transfer kermit take file "getshar"
BBC> take getshar			; transfer shell archives
BBC> *basic				; return to BASIC
>					; BASIC prompt


UNPACKING SHELL ARCHIVES

After downloading the shell archives, the Small-C ROM must be
bootstrapped, and the compiler programs must be 'unpacked' before they
can be used:

>					; BASIC prompt
> *exec mkboot				; dehex Small-C ROM, and utils
> *rload sh 14				; load Small-C ROM image in slot 14
> <break>				; initialise ROM
> *sh					; invoke tcc command shell
$					; Small-C prompt
$ exec :1.unpack			; unpack shell archives
$ access *.* L				; lock all files for safety


DOWNLOADING TCC FROM AN IBM-PC HOST

The MSDOS version of the compiler is distributed via e-mail as 'boo'
encoded archives which must be downloaded onto an IBM-PC or compatible
micro.  The files are then unpacked using the 'deboo' and 'arc'
utilities (available from Lancaster PDSoft distribution service).  The
MSDOS version of the compiler can then be used to cross-compile code for
a BBC Micro.  The DFS version of the compiler was cross-compiled on an
Amstrad PC-1512, then transferred to a BBC Micro fitted with an Aries
B32 RAM board using the following commands:

>					; BASIC prompt
> *xoff					; disable ARIES B32 shadow RAM
> <break>				; press break key
> *rload kermit 13			; load kermit ROM image in slot 13
> <break>				; initialise ROM
> *kermit				; invoke kermit
BBC>					; kermit prompt
BBC> set file type ascii cr		; setup for ascii transfer
BBC> get get get			; transfer kermit take file "get"
BBC> take get				; transfer tcc files
BBC> *basic				; return to BASIC
>					; BASIC prompt


DFS INSTALLATION

After downloading a copy of the DFS distribution disk from an MSDOS
host, the compiler programs must be 'installed' before they can be used:

>					; BASIC prompt
> *rload sh 14				; load Small-C ROM image in slot 14
> <break>				; initialise ROM
> *sh					; invoke tcc command shell
$					; Small-C prompt
$ mode 7				; set vdu mode 7
$ exec install				; set executable file attributes
$ access *.* L				; lock all files for safety


INITIAL SETUP

The system is distributed in DFS format, for use on a 'standard' BBC
Micro, but can be used under ADFS without modification.  Source programs
are edited (using VIEW or whatever editor you have), and saved to disk. 
The restricted number of files in the DFS catalogue means that sources
are normally saved in ":2.*_c", and the distributed sources can be found
on side 2 of the disk.  The distribution disk is FULL, and needs to be
reorganised in order to use the compiler.  Side 0 of the disk contains
the executable binaries, #include <files> and Small-C language ROM/RAM
image.  These files must always be present in drive 0.  The files on
side 2 must be copied to other disks in order to recompile the programs. 
The compiler program "tccom", in particular, needs a disk to itself in
order to recompile ...  Error recovery is virtually non-existent, and
DFS "can't" extend problems should be avoided by periodically
*compacting the disks. 


EXAMPLE PROGRAM

The "Towers of Hanoi" example can be compiled using the distribution disk
in BBC drive 1/3, and a blank formatted working disk in drive 0/2 as follows:
	
>					; BASIC prompt
> *drive 0				; select drive 0 on distrib. disk
> *xoff					; disable ARIES B32 shadow RAM
> *rload sh 14				; load Small-C ROM image in slot 14
> <break>				; initialise ROM
> *sh					; invoke tcc command shell
$ copy 1 0 *.*				; copy 'system' files onto working disk
$ copy 3 2 hanoi_c			; copy example source file 
$ drive 2				; select drive 2 on working disk
$ mode 7				; set vdu mode 7
$ tcc -o hanoi hanoi_c			; compile example
$ mode 2				; set vdu mode for "hanoi"
$ hanoi					; run program
$ mode 7				; reset vdu mode
$ basic					; return to BASIC
>					; BASIC prompt

	
See the description of each utility program for a detailed explanation
of how to use them.  The Small-C sources are intended to be examples of
how to use the language - if you need more help than this, consult the
excellent "Small-C Handbook" by James E.  Hendrix.  There are also
numerous Small-C programs available from the CP/M user group. 
	
	
	
	
                                 MANUAL


--------------------------------------------------------------------------------
INDEX
	as65
	cmp
	crt
	ctype
	demo
	diff
	errors
	get, put
	install
	ld
	lib
	lpr
	makefile [mktcc]
	rm
	sfa
	sh
	shar
	stdio
	sys
	tcc
	tccom
	tcpp
	unpack


--------------------------------------------------------------------------------
NAME
	as65

SYNOPSIS
	as65 [-l] [-o outfile] file1 ... [filen]

DESCRIPTION
	Assembler for the 6502 processor.  This is a two pass assembler
	that processes the concatenation of source files given as
	command-line arguments.  Local symbols are prefixed by tilde '~'
	and are not written to the global symbol output file.  Mnemonics
	are lower-case, and are reserved symbols.  Underline '_' is
	accepted as an alpha character in symbols.  Assembly language
	routines may be called from Small-C programs, provided the
	Small-C parameter passing conventions are observed.  In this
	implementation, parameters are always promoted to 16-bits with
	sign extension to the left and pushed on the data stack in
	'reverse' order.  In addition, the compiler prepends an
	underline '_' to the name of the Small-C function used to call
	the assembly language routine.  The external symbols referring
	to code in the run-time support module, and BBC MOS are passed
	to the assembler by means of equate directives in the external
	symbol file 'ext_s' or 'swext_s'.  If the Small-C 'end' symbols
	~eot (end of text) and ~eod (end of data) are present, the size
	of the text and data segments are printed in decimal, followed
	by the assembly origin, ~eot, and ~eod values in hex.  The
	assembler follows MOS Technology/Rockwell conventions.  Consult
	the manufacturer's 6502 assembly language reference manual for
	more details. 

	Options:
		-l		produce assembly language listing
		-o name		specify name of output file

	Note: The assembler can be used without an "optab" file in order
	to generate "optab" itself from .BYTE assembler pseudo-ops.  In
	this situation a warning is issued, but the assembly continues. 

BUGS
	JMP expects a 16-bit destination, and JMP's into page zero are
	wrongly flagged as errors.  This arises when the assembler
	origin is not set.  Optab is needed because there is no simple
	way of initialising static data in the current version of tcc. 
	Mnemtab is needed to pre-hash the mnemonics into the symbol
	table. 

FILES
	as65.c
	optab_s		source code to generate optab
	:0.$.optab	6502 opcode table
	:0.$.mnemtab	6502 mnemonics
	o_out		default output file
	g_out		global symbol file

	
--------------------------------------------------------------------------------
NAME
	cmp

SYNOPSIS
	cmp file1 file2

DESCRIPTION
	Simple byte by byte file comparison.

FILES
	cmp.c


--------------------------------------------------------------------------------
NAME
	crt

SYNOPSIS
	Stand-alone Small-C run-time support

DESCRIPTION
	Large programs such as the compiler "tccom" require the Small-C
	language ROM/RAM image to be present, but smaller programs can
	be made 'stand-alone' using the -A option of "tcc".  This loads
	the run-time support and compiler library in the default text
	area above the MOS high water mark at $1900 in the i/o processor
	memory area.  The default load address is set to $1902 in order
	to avoid error messages from the BASIC language ROM which
	initialises the first two bytes of this area. 

BUGS
	The entire run-time support is loaded, even though a large part
	of it may never be referenced by the user program.  A link
	editor is required. 
	
FILES
	mkcrt		*exec file to assemble crt
	oshdr_s		MOS entry points, and Small-C workspace definitions
	crt0_s		stand-alone start-up code
	crt1_s		JSR threaded code interpreter
	sys_s		operating system interface
	lib_s		part of the 'standard' C library
	patch_s		control flow patch
	ext_s		external symbol file used to link user programs
	enter_s		entry point patch for user program


--------------------------------------------------------------------------------
NAME
	ctype

SYNOPSIS
	#include <ctype.h>

DESCRIPTION
	This is a dummy file in release 0.7 - the character
	classification table is defined in sys_s, and character
	classification routines are written in assembly language. 

BUGS
	Should be done with pre-processor macros ...

FILES
	:0.$.ctype.h
	sys_s

	
--------------------------------------------------------------------------------
NAME
	demo

SYNOPSIS
	tcc -o bm bm_c
	tcc -o fahr fahr_c
	tcc -o hanoi hanoi_c
	tcc -o plot plot_c
	tcc -o sieve sieve_c

DESCRIPTION
	Small-C demonstration programs:

		bm	PCW Benchmarks
		fahr	K & R tutorial example
		hanoi	Towers of Hanoi (use VDU mode 2)
		plot	Recursive squares (use VDU mode 2)
		sieve	Sieve of Eratosthenes

BUGS
	Can't change VDU mode during program execution.

FILES
	:2.bm_c
	:2.fahr_c
	:2.hanoi_c
	:2.plot_c
	:2.sieve_c


--------------------------------------------------------------------------------
NAME
	diff

SYNOPSIS
	diff file1 file2

DESCRIPTION
	Line by line file comparison.

BUGS
	Not really diff (as in Unix), but still useful.

FILES
	diff.c


--------------------------------------------------------------------------------
NAME
	errors

SYNOPSIS
	Compiler error codes

DESCRIPTION
	Brief explanation of compiler error codes.  These have been
	deleted from the compiler to save space. 

BUGS
	There are errors in the errors ...

FILES
	:0.$.errors	list of error codes
	tccom.c		source shows where errors are detected


--------------------------------------------------------------------------------
NAME
	get, put

SYNOPSIS
	*kermit
	take get

	*kermit
	take put

DESCRIPTION
	Kermit 'take' files to download/upload "tcc" system from MSDOS
	host.  Get "get" onto the BBC Micro first, then download the
	rest of the files automatically using the Kermit take command. 
	The take files assume that the MSDOS kermit is in server mode,
	and the BBC Micro kermit is the 'local' kermit. 

BUGS
	DFS/ADFS attributes need to be set using "install"

FILES
	get		Kermit takefile
	install		*exec file to set file attributes


--------------------------------------------------------------------------------
NAME
	getshar

SYNOPSIS
	*kermit
	take getshar

DESCRIPTION
	Kermit 'take' file to download "tcc" system from remote
	host.  Get "getshar" onto the BBC Micro first, then download the
	rest of the files automatically using the Kermit take command. 
	The take files assume that the MSDOS kermit is in server mode,
	and the BBC Micro kermit is the 'local' kermit.  The shell
	archives are unpacked using the "unpack" command.

BUGS
	"getshar" assumes that two disk drives are available.

FILES
	getshar		Kermit takefile
	unpack		*exec file to unpack shell archives


--------------------------------------------------------------------------------
NAME
	install

SYNOPSIS
	exec install

DESCRIPTION
	Utility to set DFS/ADFS file attributes after downloading
	binaries with Kermit from MSDOS host. 

BUGS
	Language ROM/RAM image must already be loaded.

FILES
	sfa		executable binary of utility to set file attributes
	swcrt		Language ROM/RAM image


--------------------------------------------------------------------------------
NAME
	ld

SYNOPSIS
	ld [-o outfile] [-R] file1 ... [filen]

DESCRIPTION
	Simple loader for stand-alone binaries, and ROM images of
	Small-C programs.  No link editing is done: the loader simply
	concatenates the binaries given as arguments with the
	appropriate run-time support.  All external references are
	resolved by the assembler, using the external symbol file
	"ext_s" or "swext_s". 

	Options:
		-o outfile	specify name of output file
		-R		load sideways ROM/RAM image

BUGS
	The order of files in the argument list is critical, and
	relocation is impossible because the assembler produces absolute
	binary modules. 

FILES
	a_out		default output file
	crt		stand-alone run-time support
	swcrt		sideways ROM/RAM run-time support


--------------------------------------------------------------------------------
NAME
	lib

SYNOPSIS
	tcc -S lib.c
	exec mkcrt
	exec mkswcrt

DESCRIPTION
	Small-C compiler library.  A few of the 'standard' C library
	routines have been implemented:

		atoi(s)
		fclose(fp)
		fgets(s, n, fp)
		fopen(name, mode)
		fprintf(fp, fmt, arg)
		fputs(s, fp)
		fscanf(fp, fmt, arg)
		gets(s)
		itoa(s, radix)
		printf(fmt, arg)
		puts(s)
		scanf(fmt, arg)
		sscanf(s, fmt, arg)
		sprintf(s, fmt, arg)
		strcat(s1, s2)
		strcmp(s1, s2)
		strcpy(s1, s2)
		strlen(s)
		strncat(s1, s2, n)
		strncmp(s1, s2, n)
		strncpy(s1, s2, n)

BUGS
	There are lots more functions to implement ...

FILES
	lib.c		Small-C source
	lib_s		assembly language file used to create "crt" and
			"swcrt"


--------------------------------------------------------------------------------
NAME
	lpr

SYNOPSIS
	lpr [-p] file

DESCRIPTION
	Expands tabs into spaces (for printers that can't handle tabs),
	and paginates output if required.  Output is directed to the
	screen and printer simultaneously using the MOS VDU driver to
	enable the printer. 


	Options:
		-p	paginate output, and print header at top of page.

BUGS
	It's not a spooler - you have to wait until the printer stops.
	
FILES
	lpr.c


--------------------------------------------------------------------------------
NAME
	makefile [mktcc]
	
SYNOPSIS
	make host
	make

DESCRIPTION
	Zorland 'C' makefile for the MSDOS version of the "tcc"
	compiler.  The "host" target generates *.exe files for the MSDOS
	host system, and the default target generates 6502 binaries to
	be downloaded onto a BBC Micro using Kermit. 

BUGS
	There is no Small-C make utility.

FILES
	makefile


--------------------------------------------------------------------------------
NAME
	rm

SYNOPSIS
	rm [-f] file1 [... filen]

DESCRIPTION
	Remove the list of files given as arguments.

	Options:
		-f	force removal, even if file is locked, and don't
			complain about non-existent files

BUGS
	Wild cards are not expanded.

FILES
	rm.c


--------------------------------------------------------------------------------
NAME
	sfa

SYNOPSIS
	sfa file

DESCRIPTION
	Set file attributes under DFS/ADFS.  The load and execute
	addresses are both set to $1902. 

BUGS
	Can't specify load and exec addresses as arguments.  The file
	access attributes are correct for ADFS, but set the "lock"
	attribute in DFS. 

FILES
	sfa.c


--------------------------------------------------------------------------------
NAME
	sh

SYNOPSIS
	*sh

DESCRIPTION
	Small-C command "shell".  This is the Small-C Language ROM/RAM
	image that must be present in order to use the "tcc" compiler. 
	The *sh entry into the Small-C Language ROM/RAM allows control
	to fall through to code immediately after the run-time support. 
	This entry is patched to main() in the command shell by the -R
	option of "tcc":

		tcc -R -o sh sh_c

	The '*' in "*sh" is used by Basic to pass a command line to the
	MOS OSCLI (operating system command line interpreter).  This is
	necessary when invoking Small-C from Basic or View, but is not
	required when programs or operating system commands are invoked
	from the Small-C command shell.

BUGS
	Global variables should not be used in programs produced with
	the -R option because the compiler places data immediately after
	the program text in what would then be read-only memory. 

FILES
	swcrt		Sideways ROM/RAM run-time support
	sh.c		Small-C command shell


--------------------------------------------------------------------------------
NAME
	shar

SYNOPSIS
	shar [-a] [-x] archive file1 [... filen]

DESCRIPTION
	Unix style shell archiver for e-mail distribution of tcc system. 
	The "archive" argument specifies the name of the archive file to
	be used.  Note: only text files can be archived with shar. 

	Options:
		-a	create archive and add files
		-x	extract file from archive

BUGS
	Individual files cannot be extracted from an archive.  The entire
	contents of an archive are extracted.

FILES
	shar.c


--------------------------------------------------------------------------------
NAME
	stdio

SYNOPSIS
	#include <stdio.h>

DESCRIPTION
	'Standard' i/o header file.  Contains standard i/o channel
	definitions, and the macro definitions of putchar() and
	getchar(). 

	#define BUFSIZ 256		/* size of disk i/o buffer */
	#define NULL 0			/* null pointer of any type */
	#define EOF (-1)		/* end-of-file 'value' */
	#define stdin 0			/* standard (console) input stream */
	#define stdout 1		/* standard (console) output stream */
	#define stderr 2		/* standard (console) error stream */
	#define FILE int		/* no structures in Small-C ... */
	#define unsigned char *		/* no unsigned type in Small-C ... */

	#define getchar() getc(stdin)
	#define putchar(x) putc(x, stdout)

BUGS
	The FILE typedef cannot be implemented properly in Small-C, but
	the i/o streams are used as if they are implemented as (FILE *)
	to make Small-C a legal subset of full 'C'.  This is ok if no
	reference is made to the FILE structure other than its use to
	identify a stream in the 'f' i/o library (eg.  fprintf()). 
	
FILES
	:0.$.stdio_h


--------------------------------------------------------------------------------
NAME
	sys

SYNOPSIS
	Operating system interface

DESCRIPTION
	The interface between Small-C and the underlying BBC Micro
	Machine Operating System (MOS) is written in assembly language. 
	The entry points for low-level file i/o are modelled on their
	Unix counterparts, and the character classification routines are
	written in assembly language to increase their speed of
	execution.  Interfaces are also provided to the MOS osbyte 'fx'
	(effects), osword and osfile calls. 

	Entry points:

		Assembler	Small_C

		_open		fd = open(name, rwmode);
		_creat		fd = creat(name, pmode);
		_close		status = close(fd);
		_unlink		status = unlink(name);
		_stat		stat(name, fcb);
		_system		system(string);
		__cmdlin	address = _cmdline()
		_read		nread = read(fd, buf, count);
		_write		nwritten = write(fd, buf, count);
		_getc		c = getc(fp);
		_putc		putc(c, fp);
		_vdu		vdu(c);
		_osbyte		osbyte(type, parameters);		
		_osword		osword(type, address);
		_osfile		osfile(name, fcb, type);
		_isalpha	t = isalpha(c);
		_isupper	t = isupper(c);
		_islower	t = islower(c);
		_isdigit	t = isdigit(c);
		_isxdigi	t = isxdigit(c);
		_isspace	t = isspace(c);
		_ispunct	t = ispunct(c);
		_isalnum	t = isalnum(c);
		_isprint	t = isprint(c);
		_iscntrl	t = iscntrl(c);
		_isascii	t = isascii(c);
		_toupper	c2 = toupper(c1);
		_tolower	c2 = tolower(c1);
		_toascii	c2 = toascii(c1);
		_ctype_		char ctype_[127];

BUGS
	File descriptors (fd) are used instead of (FILE *) for getc(),
	and putc() as in the rest of Small-C.  Pmode is ignored by
	creat(), and the system has no record of which files were opened
	by the user.  This means that programs must explicitly close
	files that they open (full 'C' will normally close files opened
	by the user on exit).  The character classification routines
	should be macros that use conditional expressions.  "System"
	doesn't spawn a new process, it just passes the line to the MOS
	command line interpreter (CLI). 

FILES
	sys_s
	ext_s		stand-alone entry points
	swext_s		sideways ROM/RAM entry points

--------------------------------------------------------------------------------
NAME
	tcc

SYNOPSIS
	tcc [-o outfile] [-n] [-E] [-S] [-c] [-g] [-R] [-A] [-C] file

DESCRIPTION
	This is the Small-C compilation sequencer.  It arranges the
	various phases of the preprocessor "tcpp", compiler "tccom",
	assembler "as65" and loader "ld" according to a list of
	command-line arguments.  The sequencer generates a *exec file
	under DFS/ADFS, or a *.bat file in the MSDOS version, which is
	then executed to carry out the compilation.  By default, the
	compiler produces ROM-dependant code which makes external
	references into the Small-C language ROM. 

	Options:
		-o outfile	specify name of output file (default a_out)
		-n		don't execute *exec (*.bat) file
		-E		run preprocessor only (no compilation)
		-S		generate an assembly language output file
		-c		suppress load phase
		-g		keep the global symbol output file "g_out"
		-R		produce ROM'able code
		-A		produce 'stand-alone' code
		-C		insert 'C' source as comments
	
BUGS
	The technique of generating a *exec file is a crude alternative
	to the creation of child processes to carry out the compilation
	tasks.  This could be done in the MSDOS version, but requires
	much more effort under the Acorn MOS.  For simplicity, I have
	used the same technique in both.  Only one source file can be
	processed in this version, but the #include preprocessor
	directive can be used to combine several *.c files. 

FILES
	tcc.c
	tcpp		Small-C preprocessor
	tccom		Small-C compiler
	as65		6502 assembler
	rm		file remover
	ld		Small-C loader
	:0.$.crt	Stand-alone run-time support, and compiler library
	:0.$.swcrt	Sideways ROM/RAM run-time support, and compiler library
	:0.$.ext_s	Stand-alone external references
	:0.$.swext_s	Sideways ROM/RAM external references
	:0.$.start_s	ROM-dependant startup code
	:0.$.enter_s	Control-flow patch to main() from user entry point
	compile		*exec file produced by sequencer

--------------------------------------------------------------------------------
NAME
	tccom

SYNOPSIS
	tccom [-C] infile [outfile]

DESCRIPTION
	Tiny 'C' compiler for the MOS Technology 6502 microprocessor,
	based on "RatC", Berry and Meeking's version of the original
	Small-C compiler for the Intel 8080 by Ron Cain.  The main
	difference between RatC and Ron Cain's Small-C is the use of a
	generic processor model with two working registers instead of
	8080 architecture.  Otherwise, the two compilers are almost
	identical.  The compiler (tccom) is normally invoked by a
	compilation sequencer (tcc), which arranges the various phases
	of the pre-processor, compiler, assembler amd loader.  The
	language features supported by "tccom" are essentially the same
	as those supported by "RatC", with more complete flow-control,
	and character escape sequences implemented.  Code generation is
	'optimised' for the 6502 in a 'small' machine environment on the
	BBC Micro.  The basic strategy is to generate code for a JSR
	threaded code interpreter, but whenever possible the contents of
	the 'C' primary register are kept in the 6502 X and Y registers. 
	Two stacks are used: the 6502 hardware stack is used as the 'C'
	return stack and is used by the JSR threaded code interpreter,
	but the 'C' data stack is implemented in high memory using
	page-zero locations as a stack pointer.  This allows 'C'
	function stack-frames to be realistically large (the 6502
	hardware stack is limited to 256 bytes in page 1).  As with
	other implementations of Small-C, the language features
	supported are a (severely) restricted subset of full 'C' but I
	have made an effort to implement a legal subset that can be
	compiled with little or no modification by a full 'C' compiler. 
	Consult the "Small-C Handbook" by James.E.Hendrix for a more
	complete description of the language.  Briefly, the features
	implemented in "tcc" are:

	Options:
		-C	output source code as assembler comments

	Types:
		char	8-bit (signed) promoted to int in expressions
		char[n]	8-bit (signed) promoted to int in expressions
		char *	16-bit (unsigned)
		int	16-bit (signed)
		int[n]	16-bit (signed)
		int *	16-bit (unsigned)
		extern	accepted, but ignored by compiler

		int function()
		int *function()
		char function()
		char *function()

	Operators:
		=	assignment			(low precedence)
		|	bitwise OR
		^	bitwise XOR
		&	bitwise AND
		==	relational equal
		!=	relational not equal
		<=	relational less-than or equal
		>=	relational greater-than or equal
		>>	bitwise right shift
		<<	bitwise left shift
		+	arithmetic add
		-	arithmetic subtract
		*	arithmetic multiply
		/	arithmetic divide (integer)
		%	arithmetic remainder (integer)
		-	arithmetic negation
		*	pointer indirection
		&	address of object
		++	arithmetic increment	
		--	arithmetic decrement
		f()	function call
		a[]	array subscript			(high precedence)

	Function calls:

		direct:
			function(args);

		indirect:
			char *address;
			address = &function;
			address(args);
		
	Control-flow:

		goto label
			...
		label:

		if (expression) {
			...
		}
		else {
			...
		}

		while (expression) {
			...
		}

		do {
			...
		} while (expression);

		for (expression; expression; expression) {
			...
		}

	Literal numbers:
		ddddd	decimal (where d is 0...9)
		0ddd	octal (where d is 0...7)
		0xdddd	hexadecimal (where d is 0...F or 0...f)

	Character escapes:
		\n	newline
		\t	tab
		\b	backspace
		\r	return
		\f	form feed
		\\	backslash
		\0	NULL
		\ddd	octal character code
		\c	any other character (where c is the character)

BUGS
	Arrays of character pointers are (incorrectly) treated as arrays
	of integers.  This leads to problems recovering command line
	options prefixed by '-'.  The fix is to AND with 0xFF, and
	various programs are commented "BUG in compiler" where this is a
	problem.  The code to implement "for" fails on the commonly used
	construct "for (;;)" which is used in 'endless' loops, and the
	code generated to implement "for" needs the entire expression on
	one line of the input stream.  The same is true for function
	calls, where the entire argument list must be on one line.  The
	analysis of the "for" construct is clumsy, and needs re-writing
	to jump round the end loop action, rather than deferring code
	generation which is used at present.  The "switch" construct has
	not yet been implemented.

FILES
	tccom.c


--------------------------------------------------------------------------------
NAME
	tcpp

SYNOPSIS
	tcpp [-Dname] infile outfile

DESCRIPTION
	Small-C preprocessor, with file inclusion and conditional
	compilation directives.  The #asm ...  #endasm directive found
	on other Small-C preprocessors is deliberately omitted because
	it leads to non-portable code.  Assembly language routines are
	incorporated in Small-C programs by combining them with the
	assembler source generated by the compiler, during assembly of
	the program.  This allows machine dependencies to be hidden from
	an applications program.  The preprocessor implements a subset
	of the Unix 'C' preprocessor "cpp":

	File inclusion:

		#include <file>		file in 'standard' directory
		#include "file"		file in current directory

	Macro replacement:

		#define name
		#define name(args)

	Conditional text inclusion:

		#if constant		test for non-zero constant
			...
		#else
			...
		#endif

		#ifdef name		test for defined macro name
			...
		#else
			...
		#endif

		#ifndef name		test for undefined macro name
			...
		#else
			...
		#endif

	Options:
		-Dname			#define name on command line

BUGS
	Constant expressions cannot be used (as in #if expression), and
	the newline escape '\' is not implemented in macro definitions
	which must, therefore, be confined to a single line of text. 

FILES
	tcpp.c
	:0.$		'standard' directory for #include <file>
	:0.$.stdio.h	'standard' i/o #include file
	:0.$.ctype.h	dummy character classification #include file


--------------------------------------------------------------------------------
NAME
	unpack

SYNOPSIS
	exec unpack

DESCRIPTION
	The BBC Micro version of tcc is distributed over e-mail or BBS's
	as a collection of Unix 'shell' archives.  This is a convenient
	format for packaging up several files, and protecting them from
	e-mail systems that occasionally interpret parts of unprotected
	files as message headers.  This may cause the file to be
	corrupted, or it may fail to arrive.  The archive files should
	be downloaded onto a BBC Micro as indicated in the FILES section
	below.  An example kermit take file is provided, or the files
	can be downloaded individually.  The unpack utility assumes that
	you have a two-drive system.
	
	The 6502 binaries of the Small-C Language ROM and "shar" program
	must first be de-hexed and the "sh" file loaded into sideways
	RAM.  The unpack script uses the "shar" program to extract the
	other hexfiles from tcc1 and tcc2.  These are dehexed, and the
	remaining source files are extracted.  The resulting disk
	contains the complete tcc source distribution.  Make a copy of
	the disk before attempting to use the compiler, and delete some
	of the source files to make room for temporary files created by
	the compiler.

BUGS
	It takes a  l o n g  time to extract the files.

FILES
	:0.getshar	kermit take file to download shell archives
	:0.mkboot	*exec file to dehex Small-C boot files
	:0.sh_x		6502 hex file of Small-C Language ROM/RAM image
	:0.dehex_x	6502 hex file of Intel hex decoder
	:0.shar_x	6502 hex file of shell archive program
	:1.unpack	*exec file to unpack archives
	:1.tcc1		shell archive #1
	:1.tcc2		shell archive #2
	:3.tcc3		shell archive #3
	:3.tcc4		shell archive #4
	:2.READ_ME	tcc documentation


--------------------------------------------------------------------------------