PICF1024.GIF and PICF800.GIF

 These are two scans (1024x768 & 800x600) of a Tesla Magnifier
 designed, built, and operated by Richard Hull. The extra coil
 of the three coil system is set on top of a large HV insulator.
 The extra coil is fitted with a sophisticated discharger
 arraignment to protect the very low aspect ratio coil and to
 reduce the incidents of downward strikes back to the trans-
 mission line, which is simply an eight foot length of hard
 copper water pipe. The closely coupled primary/secondary coils
 (lower left) are sitting on top of a short plastic insulator to
 reduce the inductive effects of the concrete floor.

 This system is operating around 2 kVA, producing spark dis-
 charges in excess of six feet in length. The tank circuit
 capacitance consists of four homemade .018 microfarad caps
 rated around 10 kV pulse, with these capacitors wired in
 series/parallel so that the measured tank circuit capacitance
 is .018 microfarads rated @ 20 KVAC pulse. The power supply is
 a three kVA potential transformer ballasted with both resistive
 and inductive elements. The spark gap system consists of a large
 rotary gap specially designed for the extremely fast quenching
 required on Tesla Magnifier systems.